.BS 
\l'6i'
.BE
.deTP
'sp
.)K
.af;P \\gP
.afP 1
.nr;P \\nP
.afP \\g(;P
.af;P 1
.ie\\n(Pv \{\
.ie(\\n(Pv=1)&(\\n(;P>1) 'sp 2
.el\{\
.ce
.ul
PRIVATE
.sp\} \}
.el'sp 2
.if!\\n(;P-1 .if \\nN 'sp
.if!\\n(;P-1 .if \\n(:S .tl \\*(}t
.if!\\n(;P-1 .if !\\nN .tl \\*(}t
.if\\n(;P-1 .ie \w'\\*(]n' .tl '\\*(]n - \\nP'''
.el.tl \\*(}t
\l'6i'
.sp
..
.nr Cl 4
.nr Hs 2
.nr Hb 3
.ds HF 3 3 3 3 3 3 3
.ds HP 12 11 10 10 10 10 10
.nr Ej 1
.PH "'Novell, Inc.'Compression for Wide Area Networks''"
.PF "'Introduction'' \\\\nP'"
.H 1 "Introduction
This short paper will present a number of compression options and 
alternatives.  It is hoped that it will provide ample information to 
choose an appropriate compression algorithm and method for 
implementation in the Novell Wide Area Networking product.

It is desired to perform some type of compression on the data to be 
transmitted to a remote site to increase the apparent bandwidth of 
the (probably) low-speed link.  This compression can take many 
forms, and can be applied at one or more layers of a networking 
protocol.  In this paper, implementation at the data link layer 
will be explored.

In selecting a compression algorithm, it is necessary to consider the 
following items:

.BL
.LI
Compression ratio
.br
This is the ratio of the data emitted from the compression routine 
versus the data received by the routine.  For example, 300,000 bytes 
received and 100,000 bytes transmitted would be a 3:1 compression ratio.

.LI
Speed
.br
The algorithm's speed must be considered, 
especially when Novell protocols are involved.

.LI 
Size of memory required to implement the protocol
.br
The amount of dictionary space required in RAM for each protocol.
.LE

.H 2 "Description of Method"

To test the various compression methods, some representative 
data was required.  This data was obtained from a public domain 
collection of binary, text and image files, collected by T.C. Bell 
and J.G. Cleary.  Collectively, these files are referred to as the 
Calgary/Canterbury text compression corpus.  This corpus is used 
in the book:

.in 1i
Bell, T.C., Cleary, J.G. and Witten, I.H. Text compression.
Prentice Hall, Englewood Cliffs, NJ, 1990
.in 0

and in the survey paper

.in 1i
Bell, T.C., Witten, I.H. and Cleary, J.G. "Modeling for text
compression," Computing Surveys 21(4): 557-591; December 1989
.in 0

The corpus is used to evaluate the practical performance of various 
text compression schemes.  Several other researchers are now using the 
corpus to evaluate text compression schemes.

Nine different types of text are represented, and to confirm that 
the performance of schemes is consistent for any given type, many of 
the types have more than one representative.  Normal English, 
both fiction and non-fiction, is represented by two books and 
papers (labeled book1, book2, paper1, paper2, paper3, paper4, 
paper5, paper6).  

More unusual styles of English writing are found in a bibliography 
(bib) and a batch of unedited news articles (news). Three computer 
programs represent artificial languages (progc, progl, progp). A 
transcript of a terminal session (trans) is included to indicate 
the increase in speed that could be achieved by applying compression 
to a slow line to a terminal.  All of the files mentioned so 
far use ASCII encoding.  Some non-ASCII files are also 
included: two files of executable code (obj1, obj2), some 
geophysical data (geo), and a bit-map black and white 
picture (pic).  The file geo is particularly difficult to 
compress because it contains a wide range of data values, 
while the file pic is highly compressible because of large 
amounts of white space in the picture, represented by long 
runs of zeros.

More details of the individual texts are given in the book 
mentioned above. Both book and paper give the results of 
compression experiments on these texts.

The corpus itself constitutes files bib, book1, book2, geo, news, 
obj1, obj2, paper1, paper2, paper3, paper4, paper5, 
paper6, pic, progc, progl, progp and trans.  (The book and paper 
above do not give results for files paper3, paper4,
paper5 or paper6.)

.TB "Input File descriptions"
.TS
box, center;
l | l | l | l | l
l | l | n | n | n.
Filename	Description	Lines	Words	Characters
_
bib	Bibliographic files (refer format)	6280	19274	111261 
book1	Hardy: Far from the madding crowd	16622	141274	768771 
book2	Witten: Principles of computer speech	15634	101221	610856 
geo	Geophysical data	18	617	102400 
news	News batch file	10059	53939	377109 
obj1	Compiled code for Vax: compilation of progp	87	495	21504 
obj2	T{
Compiled code for Apple Macintosh: 
Knowledge support system
T}	1213	4600	246814
paper1	T{
Witten, Neal and Cleary: 
Arithmetic coding for data compression
T}	1250	8512	53161 
paper2	Witten: Computer (in)security	1731	13829	82199 
paper3	Witten: In search of "autonomy"	1100	7219	46526 
paper4	Cleary: Programming by example revisited	294	2166	13286 
paper5	Cleary: A logical implementation of arithmetic	320	2099	11954 
paper6	T{
Cleary: Compact hash tables using 
bidirectional linear probing
T}	1019	6753	38105 
pic	T{
Picture number 5 from the CCITT 
Facsimile test files (text + drawings)
T}	0	49	513216
progc	C source code: compress version 4.0	1487	6313	39611 
progl	Lisp source code: system software	2244	9235	71646 
progp	T{
Pascal source code: prediction by partial 
matching evaluation program
T}	1966	4847	49379 
trans	Transcript of a session on a terminal	2737	9255	93695 
Total		64061	391697	3251493
.TE


These files, on their own, do not correctly represent traffic 
between routers.  They do, however, give a good base indication of 
common types of files that are likely to occur.  To more 
closely represent real traffic, a separate program was 
written to combine all 20 of these files into a single data 
stream, with PPP (Point-to-Point Protocol); 
IPX (Internetwork Packet eXchange); and NCP 
(Netware Core Protocol) headers prepended to the data.  Data from 
each of the 20 files was read, 512 bytes at a time, until the 
data was exhausted.  The 20 separate data streams were 
linear multiplexed into a single data stream, of 3,531,333 bytes 
(including headers).  For this (contrived) example, 
the IPX and NCP overhead was about 8%.  The program in the 
following figure produced this data stream.



.FG "Makepack.c"
.ft CW
.nf
#include <stdio.h>
#include "ipx.h"
#define NUMHOSTS 18

struct NCPPACK Hosts[NUMHOSTS];

char *Files[NUMHOSTS] = {
"../files/bib","../files/book1","../files/book2","../files/geo",
"../files/news","../files/obj1","../files/obj2","../files/paper1",
"../files/paper2","../files/paper3","../files/paper4","../files/paper5",
"../files/paper6","../files/pic","../files/progc","../files/progl",
"../files/progp","../files/trans"};

unsigned long Filepos[NUMHOSTS];


main(argc,argv)
int argc;
char **argv;
{
    int x,y,done;
    FILE *fo;
    struct ipx *ipx;
    struct ncp *ncp;
    if (argc < 2) {
	fprintf(stderr,"Usage: %s outfile\n",argv[0]);
	fprintf(stderr,"Builds an output file with PPP/IPX/NCP headers 		from the standard\n");
	fprintf(stderr,"compression benchmark test\n");
	fprintf(stderr,"Version 1.00  Tue Nov 10 13:34:02 1992      		Dave Rand\n");
	exit(1);
    }
    for (x=0; x< NUMHOSTS; x++) {
	ipx = &Hosts[x].ipx;
	ipx->ipx_sum = 0xffff;
	ipx->ipx_len = 512 + sizeof(struct ncp) + sizeof(struct ipx);
	ipx->ipx_tc = 0;
	ipx->ipx_pt = NW_PROTO_NCP;
	ipx->ipx_dna.x_net = rand() + (rand() << 16);
	for (y=0; y<6; y++)
	    ipx->ipx_dna.x_node[y] = rand();
	ipx->ipx_dna.x_sock = NW_SOCK_FS;
	ipx->ipx_sna.x_net = rand() + (rand() << 16);
	for (y=0; y<6; y++)
	    ipx->ipx_sna.x_node[y] = rand();
	ipx->ipx_sna.x_sock = NW_SOCK_FS;
	ncp = &Hosts[x].ncp;
	ncp->ncp_op = NCP_REPLY;
	ncp->ncp_seq = 0;
	ncp->ncp_conn = rand();
	ncp->ncp_task = rand();
	Filepos[x] = 0L;
    }
    
    fo = fopen(argv[1],"wb");
    if (fo == NULL) {
	fprintf(stderr,"Can't open file %s for output!\n",argv[1]);
	perror(argv[0]);
	exit(2);
    }
    done = 0;
    while (done != NUMHOSTS) {
	done = 0;
	for (x=0; x < NUMHOSTS; x++) {
	    if (Filepos[x] == -1L) {
		done++;
	    } else {
		packit(Files[x],&Filepos[x],&Hosts[x],fo);
	    }
	}
    }
    fclose(fo);
}

unsigned char buf[512];
packit(file,pos,host,fo)
char *file;
unsigned long *pos;
struct NCPPACK *host;
FILE *fo;
{
    FILE *fi;
    int size;
    fi = fopen(file,"rb");
    if (fi == NULL) {
	fprintf(stderr,"Can't open %s - continuing\n",file);
	*pos = -1L;
	return(1);
    }
    fseek(fi,*pos,0);
    size = fread(buf,1,512,fi);
    if (size != 512)
	*pos = -1L;
    else
	*pos = ftell(fi);
    fprintf(fo,"\377\003");
    fwrite(host,sizeof(struct NCPPACK),1,fo);
    fwrite(buf,size,1,fo);
    host->ncp.ncp_seq++;
    fclose(fi);
}
.R
.fi



.PF "'Test Results'' \\\\nP'"
.H 1 "Test Results"

The results of running the various compress programs are 
presented in the following table. 

.TB "Test results"
.TS
box,center;
l | l | l | l | l | l | l | l
l | l | n | n | n | n | n | n.
Compression Program	Method	Max ratio	Output size	Ratio	Time	K/sec	RGF
_
HPACKA 0.75c0	LZA		1272999	2.774	307	11.50	4146
Info-ZIP 1.9	LZSSA	905	1297993	2.721	90	39.24	14422
Gandalf FZA 	FZA		1310367	2.695	
ARJ 2.30NG	LZSSA	1658	1313249	2.689	58	60.89	22642
LHA 2.13	LZAH	1883	1470858	2.401	66	53.51	22286
AR002	LZAH	1859	1470865	2.401	176	20.06	8357
HYPACK 2.5	LZAH	23810	1528534	2.310	47	75.13	32522
PKZIP 1.10	LZSF	519	1549210	2.279	53	66.63	29231
Unix COMPRESS	LZW	550	1580342	2.235
LZ	LZH	48	1641731	2.151	274	12.89	5992
DWC A5.01	LZW	532	1747822	2.020	11	321.03	158892
UNIX ARC	LZW	541	1872769	1.886
PKPAK 3.61	LZW	541	1912705	1.846	19	185.86	100668
LARC 3.33	LZSS	8	1914044	1.845	84	42.04	22786
MDCD 1.00	LZW	515	1917596	1.842	35	100.90	54788
ZOO 2.10	LZW	503	1917643	1.841	80	44.14	23971
SQZ 1.08.2	LZW		1937345	1.823	270	13.08	7175
STAC 3.1 /p255	LZS	30	1949600	1.811	22	160.52	88618
Sea ARC	LZW	3003	2024142	1.745
PRED 1.02	Prediction	8	2117640	1.668	5	706.27	423728
V.42bis (12 bit)	LZW	471	2274812	1.552	65	54.39	34997
STAC 3.1 /p0	LZS	30	2314985	1.525	13	271.64	178076
NSWP3 1.020	RLE-Huffman	336	2339012	1.510	46	76.77	50848
SPLAY 1.00	Splay-tree	8	2426472	1.455	71	49.74	34176
RLE 1.00	RLE-only	86	3157471	1.118	5	706.27	631494
Original input file			3531333	1.000
.TE

Compression program is the program used to evaluate the particular 
compression method.  Notice that the same algorithm implemented by 
different programs can produce different results.  This 
usually reflects the programmer's choice of string search algorithm.

Method is the generic compression method applied to the input file.

Max ratio is the best-case compression ratio of the algorithm 
expressed. It was determined by compressing a 1,000,000 byte 
file filled with hex 00 characters.

Output size is the total output file size, including any 
header information required to correctly decompress the file.

Time is the time required to compress the given file. In all 
cases, decompression time was significantly better than 
compression time, and is therefore not given in this table.

K/sec is the Kilobytes per second rate of the algorithm, as 
seen from the input side (the ratio of the input file size 
and the execution time).

RGF is the Rand Goodness Factor for the particular algorithm. 
Higher numbers are better, and (coincidentally) 
illustrate the expected bytes-per-second of output bandwidth 
achievable with each implementation. For example, a 
RGF of 4,146 would be an excellent choice for a 19,200 
bps async modem channel, but not very effective on a T1 
(throughput would be lower than without compression, 
on this test data). The RGF is not a cure-all number; the 
compression ratio, the destination link bandwidth, and 
the input data set must be considered.

All of these algorithms, in their current form 
(most of them are implemented in C or Pascal) are capable of 
performing well on a <64Kbps link. The slower 
algorithms (LHA) will show an adequate-to-very good 
compression ratio.  Faster links are a problem, however. 
Few of the algorithms in their current form are adequate 
for medium to high speed links (>1Mbps, <10Mbps). 


.PF "'Link issues'' \\\\nP'"
.H 1 "Link issues

For any of these compression algorithms to be implemented, a 
reliable link between the source and destination 
must be implemented.  This is required due to the 
fact that even a one bit change in the compressed data stream 
may affect hundreds or thousands of bytes in the 
decompressed data stream.  

There are many forms of reliable data delivery systems 
available.  I suggest that the best one for the task at hand is 
the LAPB (Link Access Protocol B) standard.  This 
protocol has low overhead, known robustness, and is quite easy 
to implement.  It is also the protocol under review by the 
PPP compression group - though not accepted as a 
standard at this time.

In order to maximize the bandwidth of the link, and to 
allow for dynamic and transparent on-demand allocation of 
additional dial-up links (including load sharing), the 
upper-level packet structure will NOT be maintained through 
to the data link level.  Since a packet may (potentially) 
compress to just a few bits, it is worthwhile to re-packetize 
the data. This offers better line utilization 
(due to larger 2K packets), lower per-packet overhead, with 
no increase in latency.

By observing the `backlog' of packets outstanding to 
send on a link, line utilization figures can be obtained.  When 
the line utilization is at (for example) 150%, a new link 
can be established to the target system.  As more and more 
links are established to the target system, the bandwidth 
increases linearly.  By watching the highest-numbered line 
(most recently established) traffic, that link can be 
closed when the traffic through it falls below some threshold 
level.  Notice as well that latency is reduced somewhat as 
additional links are added.  Links that are dropped due to 
line failure need not be re-established, unless they are 
the only link to the target system.  Outbound traffic is always 
sent starting at the lowest numbered line (least 
recently established), and traffic is sent through additional lines 
only if warranted.

The following figure shows a single link in action

.FG "Data Compressor Diagram

(not included)

 
As can be seen, the data compressor resides in the TSM.  
This allows the TSM to open and establish additional 
links to the target system by connecting to additional WHSM's.

Data will be sent to the compressor in the form of a 
two-byte (network order) length ( of data in packet), the 
contents of the packet, and a CRC-16 as found in RFC-1331. The 
cost of computing this CRC is less than 0.5 
milliseconds for a 1.5K input packet.  The addition of the 
CRC-16 permits the compress/decompress pair to know 
when they are out of synchronization, and force a 
reset operation. It also allows for errors that may occur between 
the WHSM and the TSM.

LAPB will be performed with CRC-32, as found in the 
LAPB specification.  This ensures the maximum reliability 
in data transmission between source and destination, with a very 
slight (<0.1 %) increase in data size.  In the case 
of synchronous data transmission, it will also offer faster 
throughput due to software calculation of the CRC.  In 
the current hardware, it will provide almost a 2% increase in speed.


.H 2 "CRC 16/CRC 32 Computation Overhead"

CRC 16 can also be referred to as the HDLC FCS, or more 
properly, CRC-CCITT.  As described in RFC-1331, this 
expresses the polynomial (omitted).  CRC 16 is useful for catching 
all single bit, all two bit, most 
burst errors of less than 16 bits, and some larger 
errors in data streams of less than 32,767 bits in length (4K byte 
frames), with a failure rate of 0.0015%.  Multi-bit 
errors drastically reduce its effectiveness.

CRC 32 catches all single bit, two bit, and burst errors 
less than 31 bits. In packets of less than 2,147,483,648 bits 
(256 Mbytes), it catches larger errors with a failure 
rate of  0.0000000023%. It expresses the polynomial (omitted). 
CRC 32 is used commonly in Ethernet applications, and (while it 
looks more complex) is just as easy to compute as CRC 16.  

To compute CRC 16, one initializes a table of possible 
results of each of the 256 possible input states, initializes a 
variable to 0xFFFF, and iterates over the data with the following code:

.ft CW
fcs = (fcs >> 8) ^ fcstab[(fcs ^ DATA_BYTE) & 0xff];
.R

When all of the data has been fed through the CRC generator, the 
variable fcs will contain the CRC 16 value for the code. It is normal 
practice to complement this, and append it to the data. In the 
case of CRC 16, when this is done the appended (complemented) CRC 
can also be fed through the CRC generator. If the result of this is 
0xF0B8, the frame is good.  The CRC can also be compared to the CRC 
in the stream, and not run through the CRC generator (if desired).

An implementation of this in 8086 assembler would be as follows:

.ft CW
.nf
; AL has new byte to be computed
;
	mov	cx,fcs		; get current FCS value
	mov	bl,cl		; get lsb of fcs
	xor	bl,al		; xor in current data byte
	xor	bh,bh		; value is in the range 00-FF
	shl	bx,1		; multiply bx by 2 to get word index
	mov	ax,fcstab[bx]	; get new value from table
	xor	al,ch		; xor old fcs value
	mov	fcs,ax		; save current fcs

.R
.fi


In theory, this code should run in (1+1+1+1+1+1+1 = 7) 7 clocks on a 
486, for a throughput of 4.7 megabytes per second (or about 325 
microseconds for a 1.5Kbyte packet) on a 33 MHz 486 system. 
On an 8088, this routine takes (19 +2+2+2+2+22+19 = 68) 68 clocks, 
for a throughput of 70 Kbytes/sec (or 22 milliseconds for a 1.5Kbytes 
packet). Note that in the case of the 486, the throughput 
exceeds that of the ISA bus. Of course, this can be 
optimized - placing the FCS in a register will raise the
throughput to 6.6 Meg/sec; using 32 bit instructions will 
raise throughput to 8.25 Meg/sec.


To compute CRC 32, one initializes a table of possible 
results of each of the 256 possible input states, initializes a 
variable to 0xFFFFFFFF, and iterates over the data with the 
following code:

.ft CW
fcs = (fcs >> 8) ^ fcstab32[(fcs ^ DATA_BYTE) & 0xff];
.R

When all the data has been fed through the CRC generator, 
the variable fcs will contain the CRC 32 value for the 
code. It is normal practice to complement this, and append it 
to the data. In the case of CRC 32, when this is done 
the appended (complemented) CRC can also be fed through the 
CRC generator. If the result of this is 0xDEBB20E3, the frame 
is good.  The CRC can also be compared to the CRC in the stream, 
and not run through the CRC generator (if desired).

An implementation of this in 8086 assembler would be as follows:

.ft CW
.nf
; AL has new byte to be computed
;
	mov	cx,fcs		; get lsw of current FCS value
	mov	dx,fcs+2		; get msw of FCS
	mov	bl,cl		; get lsb of fcs
	mov	cl,ch		; shift FCS right 8 bits
	mov	ch,dl		; dh has msb
	xor	bl,al		; xor in current data byte
	xor	bh,bh		; value is in the range 00-FF
	shl	bx,1		; multiply by 4 as
	shl	bx,1		; each entry is 1 doubleword
	xor	cx,fcstab[bx]	; xor table with old fcs value
	mov	fcs,cx		; save current fcs
	mov	ax,fcstab+2[bx] ; get msw of fcstable
	xor	al,dh		; xor with old fcs value
	mov	fcs+2,ax		; save result
.R
.fi

In theory, this code should run in (1+1+1+1+1+1+1+1+1+1+1+1+1+1 = 14) 
14 clocks on a 486, for a throughput of 2.4 megabytes per second 
(or about 651 microseconds for a 1.5Kbyte packet) on a 33 MHz 
486 system. On an 8088, this routine takes 
(19+19+2+2+2+2+2+2+2+22+19+22+2+19 = 136) 136 clocks, for a 
throughput of 35 Kbytes/sec (or 44 milliseconds for a 1.5Kbytes 
packet).  Of course, this can be optimized - placing the FCS in a 
register will raise the throughput to 3.3 Meg/sec; 
using 32 bit instructions will raise throughput to 8.25 Meg/sec.


.PF "'Recommendations'' \\\\nP'"
.H 1 "Recommendations

I suggest that at least three algorithms be used to perform the 
compression.  The choice of the algorithm should be 
made based on the aggregate speed of the data link to the 
target system, with override capability by a configuration 
option.  The following table illustrates the recommendation.

.TB "Compression recommentations"
.TS
box,center;
l | l | l | l.
Line speed	Compression algorithm	Compression ratio	Effective speed / Max speed
_
<= 64Kbps	LZSSA	2.721	174 Kbps / 58 Mbps
<= 2 Mbps	LZW (max cw 16 bits)	2.235	4.5 Mbps / 1100 Mbps
<=10 Mbps	RLE	1.668	16.7 Mbps /  80 Mbps
.TE

The maximum speed is the theoretical maximum 
compression ratio for the algorithms specified.  It is extremely 
unlikely that these speeds would ever be seen in practice.  
The effective speed shows the speed that could be 
obtained running at the maximum specified line speed, 
with the sample data stream detailed in the method section 
of this document.  Real, effective speeds will (of course) 
depend on the data set. Fully random data will achieve 
effective line speeds of approximately 90% of available 
bandwidth (ignoring hardware limitations).


.PF "'Background Material'' \\\\nP'"
.H 1 "Background Material

The following material was written by Haruhiko Okumura, and 
gives some background on each of the various compression algorithms.

.ce
Data Compression Algorithms of LARC and LHarc

.H 2 Introduction

In the spring of 1988, I wrote a very simple data 
compression program named LZSS in C language, and uploaded 
it to the Science SIG (forum) of PC-VAN, Japan's biggest 
personal computer network.
 
That program was based on Storer and Szymanski's 
slightly modified version of one of Lempel and Ziv's 
algorithms.  Despite its simplicity, for most files its 
compression outperformed the archivers then widely used. 
Kazuhiko Miki rewrote my LZSS in Turbo Pascal and 
assembly language, and soon made it evolve into a complete 
archiver, which he named LARC.
 
The first versions of LZSS and LARC were rather slow.  
So I rewrote my LZSS using a binary tree, and so did 
Miki.  Although LARC's encoding was slower than the 
fastest archiver available, its decoding was quite fast, and 
its algorithm was so simple that even self-extracting 
files (compressed files plus decoder) it created were usually 
smaller than non-self-extracting files from other archivers. 

Soon many hobby programmers joined the archiver project 
at the forum. Very many suggestions were made, and 
LARC was revised again and again. By the summer of 1988, 
LARC's speed and compression have improved so 
much that LARC-compressed programs were beginning to be 
uploaded in many forums of PC-VAN and other 
networks. 

In that summer I wrote another program, LZARI, which 
combined the LZSS algorithm with adaptive arithmetic 
compression.  Although it was slower than LZSS, its 
compression performance was amazing. Miki, the author of 
LARC, uploaded LZARI to NIFTY-Serve, another big 
information network in Japan.  In NIFTY-Serve, Haruyasu 
Yoshizaki replaced LZARI's adaptive arithmetic 
coding with a version of adaptive Huffman coding to increase 
speed.  Based on this algorithm, which he called LZHUF, he 
developed yet another archiver, LHarc. 

In what follows, I will review several of these 
algorithms and supply simplified codes in C language. 

.H 2 "Simple coding methods

Replacing several (usually 8 or 4) "space" 
characters by one "tab" character is a very primitive method for data 
compression.  Another simple method is run-length coding, which 
encodes the message "AAABBBBAACCCC" 
into "3A4B2A4C", for example. 

.H 3 "LZSS coding"

This scheme is initiated by Ziv and Lempel [1].  A 
slightly modified version is described by Storer and Szymanski 
[2].  An implementation using a binary tree is proposed by 
Bell [3].  The algorithm is quite simple: Keep a ring 
buffer, which initially contains "space" characters only.  
Read several letters from the file to the buffer.  Then 
search the buffer for the longest string that matches 
the letters just read, and send its length and position in the 
buffer.  If the buffer size is 4096 bytes, the position 
can be encoded in 12 bits.  If we represent the match length in 
four bits, the <position, length> pair is two bytes long.  If 
the longest match is no more than two characters, then 
we send just one character without encoding, and restart 
the process with the next letter.  We must send one extra 
bit each time to tell the decoder whether we are sending a 
<position, length> pair or an unencoded character.
 
The accompanying file LZSS.C is a version of this algorithm.  
This implementation uses multiple binary trees to 
speed up the search for the longest match.  All the 
programs in this article are written in draft-proposed ANSI C.  I 
tested them with Turbo C 2.0. 

.H 3 "LZW coding

This scheme was devised by Ziv and Lempel [4], and 
modified by Welch [5]. The LZW coding has been adopted 
by most of the existing archivers, such as ARC and PKZIP.  The 
algorithm can be made relatively fast, and is 
suitable for hardware implementation as well. 

The algorithm can be outlined as follows: Prepare a 
table that can contain several thousand items.  Initially register 
in its 0th through 255th positions the usual 256 characters.  
Read several letters from the file to be encoded, and 
search the table for the longest match.  Suppose the 
longest match is given by the string "ABC".  Send the position 
of "ABC" in the table.  Read the next character from the 
file.  If it is "D", then register a new string "ABCD" in the 
table, and restart the process with the letter "D".  If the 
table becomes full, discard the oldest item or, preferably, 
the least used.  A Pascal program for this algorithm is 
given in Storer's book [6].
 
.H 3 "Huffman coding"

Classical Huffman coding was invented by 
Huffman [7].  A fairly readable account is given in Sedgewick [8]. 

Suppose the text to be encoded is "ABABACA", with 
four A's, two B's, and a C.  We represent this situation as 
follows:

.ft CW
.nf
	4	2    1
	|	|    |
	A	B    C
.fi
.R

Combine the least frequent two characters into one, 
resulting in the new frequency 2 + 1 = 3:

.ft CW
.nf
	4	  3
	|	 / \\
	A	B   C
.fi
.R

Repeat the above step until the whole characters combine into a tree:

.ft CW
.nf
 	         7
 	        / \\
               /   3
              /   / \\
             A   B   C

.R
.fi

Start at the top ("root") of this encoding tree, and 
travel to the character you want to encode.  If you go left, send a 
"0"; otherwise send a "1".  Thus, "A" is encoded by "0", "B" 
by "10", "C" by "11". Altogether, "ABABACA" will 
be encoded into ten bits, "0100100110". 

To decode this code, the decoder must know the encoding tree, 
which must be sent separately.
 
A modification to this classical Huffman coding is the 
adaptive, or dynamic, Huffman coding.  See, e.g., Gallager 
[9].  In this method, the encoder and the decoder processes 
the first letter of the text as if the frequency of each 
character in the file were one, say.  After the first 
letter has been processed, both parties increment the frequency of 
that character by one.  For example, if the first letter is 'C', 
then freq['C'] becomes two, whereas every other 
frequencies are still one. Then the both parties 
modify the encoding tree accordingly.  Then the second letter will 
be encoded and decoded, and so on. 

.H 3 "Arithmetic coding

The original concept of arithmetic coding is 
proposed by P.  Elias.  An implementation in C language is described 
by Witten and others [10]. 

Although the Huffman coding is optimal if each character 
must be encoded into a fixed (integer) number of bits, 
arithmetic coding wins if no such restriction is made. As 
an example we shall encode "AABA" using arithmetic 
coding.  For simplicity suppose we know beforehand that 
the probabilities for "A" and "B" to appear in the text are 
3/4 and 1/4, respectively. 

Initially, consider an interval:

.ft CW
	0 <=  x  < 1.
.R

Since the first character is "A" whose probability is 3/4, 
we shrink the interval to the lower 3/4:

.ft CW
	0 <=  x  < 3/4.
.R

The next character is "A" again, so we take the lower 3/4:

.ft CW
	0 <=  x  < 9/16.
.R

Next comes "B" whose probability is 1/4, so we take the upper 1/4:

.ft CW
       27/64 <=  x  < 9/16,
.R

because "B" is the second element in our alphabet, {A, B}.  
The last character is "A" and the interval is

.ft CW
       27/64 <=  x  < 135/256, 
.R

which can be written in binary notation 

.ft CW
  0.011011 <= x  < 0.10000111.
.R

Choose from this interval any number that can be represented in 
fewest bits, say 0.1, and send the bits to the right 
of "0."; in this case we send only one bit, "1".  Thus we have 
encoded four letters into one bit! With the Huffman 
coding, four letters could not be encoded into less than four bits. 

To decode the code "1", we just reverse the process: First, 
we supply the "0." to the right of the received code "1", 
resulting in "0.1" in binary notation, or 1/2.  Since this 
number is in the first 3/4 of the initial interval 0 <= x < 1, 
the first character must be "A".  Shrink the interval into the 
lower 3/4.  In this new interval, the number 1/2 lies in 
the lower 3/4 part, so the second character is again "A", and so 
on.  The number of letters in the original file must 
be sent separately (or a special 'EOF' character must be 
appended at the end of the file). 

The algorithm described above requires that both the 
sender and receiver know the probability distribution for the 
characters.  The adaptive version of the algorithm removes this 
restriction by first supposing uniform or any 
agreed-upon distribution of characters that approximates the 
true distribution, and then updating the distribution 
after each character is sent and received. 

.H 3 "LZARI

In each step the LZSS algorithm sends either a 
character or a <position, length> pair.  Among these, perhaps 
character "e" appears more frequently than "x", 
and a <position, length> pair of length 3 might be commoner than 
one of length 18, say.  Thus, if we encode the more frequent 
in fewer bits and the less frequent in more bits, the 
total length of the encoded text will be diminished.  
This consideration suggests that we use Huffman or arithmetic 
coding, preferably of adaptive kind, along with LZSS. 

This is easier said than done, because there are many 
possible <position, length> combinations.  Adaptive 
compression must keep running statistics of frequency distribution.  
Too many items make statistics unreliable. 
What follows is not even an approximate solution to the 
problem posed above, but anyway this was what I did in 
the summer of 1988. 

I extended the character set from 256 to three-hundred or 
so in size, and let characters 0 through 255 be the usual 
8-bit characters, whereas characters 253 + n represent that 
what follows is a position of string of length n, where n 
= 3, 4 , ....  These extended set of characters will be 
encoded with adaptive arithmetic compression. I also observed 
that longest-match strings tend to be the ones that were 
read relatively recently.  Therefore, recent positions should 
be encoded into fewer bits.  Since 4096 positions are too 
many to encode adaptively, I fixed the probability 
distribution of the positions "by hand." The distribution 
function given in the accompanying LZARI.C is rather 
tentative; it is not based on thorough experimentation.  In 
retrospect, I could encode adaptively the most significant 
6 bits, say, or perhaps by some more ingenious method adapt 
the parameters of the distribution function to the 
running statistics. 

At any rate, the present version of LZARI treats the 
positions rather separately, so that the overall compression is 
by no means optimal. Furthermore, the string length threshold 
above which strings are coded into <position, 
length> pairs is fixed, but logically its value must 
change according to the length of the <position, length> pair we 
would get. 

.H 3 "LZHUF

LZHUF, the algorithm of Haruyasu Yoshizaki's 
archiver LHarc, replaces LZARI's adaptive arithmetic coding with 
adaptive Huffman.  LZHUF encodes the most significant 6 bits 
of the position in its 4096-byte buffer by table 
lookup.  More recent, and hence more probable, positions are 
coded in less bits.  On the other hand, the remaining 
6 bits are sent verbatim.  Because Huffman coding encodes 
each letter into a fixed number of bits, table lookup can 
be easily implemented. Though theoretically Huffman cannot 
exceed arithmetic compression, the difference is very 
slight, and LZHUF is fairly fast. 

The accompanying file LZHUF.C was written by Yoshizaki.  
I translated the comments into English and made a 
few trivial changes to make it conform to the ANSI C standard.
 
.H 2 "References

.nf
[1] J. Ziv and A. Lempel, IEEE Trans. IT-23, 337-343 (1977).
[2] J. A. Storer and T. G. Szymanski, J. ACM, 29, 928-951 (1982).
[3] T. C. Bell, IEEE Trans. COM-34, 1176-1182 (1986).
[4] J. Ziv and A. Lempel, IEEE Trans. IT-24, 530-536 (1978).
[5] T. A. Welch, Computer, 17, No.6, 8-19 (1984).
[6] J. A. Storer, Data Compression: Methods and Theory (Computer Science Press, 1988).
[7] D. A. Huffman, Porch IRE 40, 1098-1101 (1952).
[8] R. Sedgewick, Algorithms, 2nd ed. (Addison-Wesley, 1988).
[9] R. G. Gallager, IEEE Trans. IT-24, 668-674 (1978).
[10] I. E. Witten, R. M. Neal, and J. G. Cleary, Commun. ACM 30, 520-540 (1987).

.fi


.PF "'Legal Issues'' \\\\nP'"
.H 1 "Legal Issues

Regretfully, no compression algorithms are free of patent 
contention. The following items come from the 
comp.compression frequently asked questions list. I make 
no claims as to the validity of any of the patent issues, 
nor of any of the implementations under investigation.

.BL
.LI
Run length encoding
.br
Tsukiyama has two patents on run length encoding: 4,586,027 
and 4,872,009 granted in 1986 and 1989 
respectively. The first one covers run length encoding in its 
most primitive form: a length byte followed by the 
repeated byte. The second patent covers the 'invention' of 
limiting the run length to 16 bytes and thus the encoding 
of the length on 4 bits.  Here is the start of claim 1 of 
patent 4,872,009, just for pleasure:

1. A method of transforming an input data string comprising a 
plurality of data bytes, said plurality 
including portions of a plurality of consecutive data 
bytes identical to one another, wherein said data bytes 
may be of a plurality of types, each type representing 
different information, said method comprising the 
steps of: [...]


.LI 
LZ77
.br
The Gibson & Graybill patent 5,049,881 covers the 
LZRW1 algorithm previously discovered by Ross Williams. 
Claims 4 and 12 are very general and could be interpreted 
as applying to any LZ algorithm using hashing 
(including all variants of LZ78):

4. A compression method for compressing a stream of 
input data into a compressed stream of output data 
based on a minimum number of characters in each input 
data string to be compressed, said compression 
method comprising the creation of a hash table, 
hashing each occurrence of a string of input data and 
subsequently searching for identical strings of input data 
and if such an identical string of input data is 
located whose string size is at least equal to the minimum 
compression size selected, compressing the 
second and all subsequent occurrences of such identical 
string of data, if a string of data is located which 
does not match to a previously compressed string of data, 
storing such data as uncompressed data, and for 
each input strings after each hash is used to find a 
possible previous match location of the string, the 
location of the string is stored in the hash table, 
thereby using the previously processed data to act as a 
compression dictionary.

Claim 12 is identical, with 'method' replaced 
with 'apparatus'. Since the 'minimal compression size' can be as small 
as 2, the claim could cover any dictionary technique of the 
LZ family. However the text of the patent and the other 
claims make clear that the patent should cover the LZRW1 
algorithm only.

The following papers, published before the patent was 
filed, describe applications of hashing to LZ77 compression:

Brent, R.P.  "A Linear Algorithm for Data Compression", 
Australian Computer Journal, Vol.19, No.2 (May 
1987), p.64.

Bell, T. "Longest match string searching for Ziv-Lempel 
compression" Res. Rept. 6/89, Dept. of Computer 
Science, Univ. of Canterbury, New Zealand (Feb 89).


Phil Katz, author of pkzip, also has a patent on 
LZ77 (5,051,745) but the claims only apply to sorted hash tables, 
and when the hash table is substantially smaller than the window size.

Robert Jung, author of 'arj', has recently been granted 
patent 5,140,321 for one variation of LZ77 with hashing.  
This patent covers the LZRW3-A algorithm, also previously 
discovered by Ross Williams. LZRW3-A was posted
on comp.compression on July 15, 1991. The patent was 
filed two months later on Sept 4, 1991. (The US patent 
system allows this because of the 'invention date' rule.)

Fiala and Greene obtained in 1990 a patent (4,906,991) on 
all implementations of LZ77 using a tree data structure. 
Claim 1 of the patent is much broader than the algorithms 
published by Fiala and Greene in Comm.ACM, April 
89. The patent covers the algorithm published by Rodeh 
and Pratt in 1981 (J. of the ACM, vol 28, no 1, pp 16-24).  
It also covers the algorithm previously patented by 
Eastman-Lempel-Ziv (4,464,650), and the algorithms used in 
lharc, lha and zoo.

IBM patented (5,001,478) the idea of combining a 
history buffer (the LZ77 technique) and a lexicon (as in LZ78).


.LI 
LZ78
.br
The LZW algorithm used in 'compress' is patented 
by IBM (4,814,746)   and Unisys (4,558,302). It is also used in 
the V.42bis compression  standard and in Postscript Level 2. 
(Unisys sells the license to modem manufacturers for 
a onetime $25,000 fee.) The IBM patent application was filed 
three weeks before that of Unisys, but the US patent 
office failed to recognize that they covered the same 
algorithm. (The IBM patent is more general, but its claim 7 is 
exactly LZW.)

AP coding is patented by Storer (4,876,541).

.LI
Other data compression algorithms
.br
IBM holds a patent on the Q-coder implementation of 
arithmetic coding.  The arithmetic coding option of the 
JPEG standard requires use of the patented algorithm.  No 
JPEG-compatible method is possible without infringing 
the patent, because what IBM actually claims rights to is 
the underlying probability model (the heart of an 
arithmetic coder).

Bacon has patented (4,612,532) some form of Markov modeling.

.LE

As can be seen from the above list, all the most popular 
compression programs (compress, pkzip, zoo, lha, arj) are 
now covered by patents. (This says nothing about the 
validity of these patents.)

Here are some references on data compression patents. A 
number of them are taken from the list maintained by 
Michael Ernst <mernst@theory.lcs.mit.edu> in 
mintaka.lcs.mit.edu:/mitlpf/ai/patent-list (or patent-list.Z).

4.464.650	
.br
Apparatus and method for compressing data signals and 
restoring the compressed data signals. Inventors Lempel, 
Ziv, Cohn, Eastman. Assignees Sperry Corporation and AT&T 
Bell Laboratories. Filed 8/10/81, granted 8/7/84

4,558,302
.br
High speed data compression and decompression apparatus and 
method. Inventor Welch. Assignee Sperry 
Corporation (now Unisys). Filed 6/20/83, granted 12/10/85. The 
text for this patent can be ftped from 
rusmv1.rus.uni-stuttgart.de (129.69.1.12) in 
/info/comp.patents/US4558302.Z.

4,586,027
.br
Method and system for data compression and 
restoration. Assignee Hitachi, inventor Tsukimaya et al. Filed 
08/07/84, granted 04/29/86

4,612,532
.br
Inventor Bacon. Granted 9/1986

4,814,746
.br
Data compression method. Inventors Victor S. Miller, 
Mark N. Wegman. Assignee IBM. Filed 8/11/86, granted 
3/21/89. A previous application was filed on 6/1/83, 
three weeks before the application by Welch (4,558,302)

4,872,009
.br
Method and apparatus for data compression and restoration. 
Assignee Hitachi, inventor Tsukimaya et al. Filed 
12/07/87, granted 10/03/89.

4,876,541
.br
Stem [sic] for dynamically compressing and decompressing 
electronic data. Inventor James A. Storer. Assignee 
Data Compression Corporation. Filed 10/15/87, granted 10/24/89

4,955,066
.br
Compressing and Decompressing Text Files. 
Inventor Notenboom, L.A. Assignee Microsoft. Filed  10/13/89, 
granted 09/04/90.

5,001,478
.br
Method of Encoding Compressed Data. Filed 12/28/89, 
granted 03/19/91. Inventor Michael E. Nagy. Assignee IBM.

5,049,881
.br
Apparatus and method for very high data rate-compression 
incorporating lossless data compression and expansion 
utilizing a hashing technique. Inventors Dean K. Gibson, 
Mark D. Graybill. Assignee Intersecting Concepts, Inc. 
Filed 6/18/90, granted 9/17/91.

5,051,745
.br
String searcher, and compressor using same. 
Inventor  Phillip W. Katz (author of pkzip). Filed  8/21/90, granted 
9/24/91.

4,906,991
.br
Textual substitution data compression with 
finite length search window. Inventors Fiala,E.R., and Greene,D.H. 
Filed 4/29/1988, granted 3/6/1990. Assignee Xerox Corporation.

5,109,433
.br
Compressing and decompressing text files. Assignee Microsoft.

5,140,321
.br
Data compression/decompression method and apparatus. 
Filed 9/4/91, granted 8/18/92. Inventor Robert Jung. 
Assignee Prime Computer


Abbreviations for the compression method are: 
Huffman - Dynamic Huffman coding; RLE - Run Length 
Encoding; LZW - Lempel-Ziv-Welch dictionary coding; 
LZH - Lempel-Ziv static Huffman coding; LZSF - 
Lempel-Ziv with Shannon-Fano tree coding; 
LZAH - Lempel-Ziv with Adaptive Huffman coding; LZA - Lempel-
Ziv with Arithmetic coding; 
LZSS - Lempel-Ziv, as modified by Storer and Szymanski; 
LZSSA - LZSS with 
adaptive coding.

  Time to run algorithm on an AST 486/33, excluding file I/O time.

.SK
.R
.fi
.BS
.BE
.deTP
'sp
.)K
.af;P \\gP
.afP 1
.nr;P \\nP
.afP \\g(;P
.af;P 1
.ie\\n(Pv \{\
.ie(\\n(Pv=1)&(\\n(;P>1) 'sp 2
.el\{\
.ce
.ul
PRIVATE
.sp\} \}
.el'sp 2
.if!\\n(;P-1 .if \\nN 'sp
.if!\\n(;P-1 .if \\n(:S .tl \\*(}t
.if!\\n(;P-1 .if !\\nN .tl \\*(}t
.if\\n(;P-1 .ie \w'\\*(]n' .tl '\\*(]n - \\nP'''
.el.tl \\*(}t
.sp
..
.PH
.SK
.TC 4 1 2 0
.SK
.PF
.rs
.sp 2i
.ns
.S 20
.B
.ad r
Data Compression for 
.sp 10p
Wide Area Networks
.S
.R
.sp 2i
Revision 1.01   \n(mo/\n(dy/\n(yr
.sp 1.5i
Dave Rand
.br
Novell, Inc.
.br
San Jose, California
.sp 0.5i
.I