Latency and Transport Delay
---------------------------

In visual simulation the terms "latency" and "transport delay" refer
to the same thing -- the time elapsed between stimulus and response.
Confusion can enter the picture because there are several important
latencies in visual simulation and often it's not clear which one is
being discussed, that is, which stimulus and which response.

The most general measure is the TOTAL LATENCY, which measures the time 
between user input (such as a pilot moving a control) to display of a 
new image computed using that input. An example would be a sudden roll 
after smooth level flight. How long does it take for a tilted horizon 
to appear?

The answer to the total time required is the sum of each latency in 
the simulation system. The component latencies are usually:

  1. input device measurement and reporting latency
  2. vehicle dynamics computation latency
  3. image generation computation latency 
  4. display system (video) scan-out latency

This is the latency that matters to the user of the system, since the
overall latency is what controls the sense of realness the system can
provide.

Despite the utility of a total system measure, vendors of subsystems
can only provide latency measures for their component. The exception
to this is the image generation system, since the video latency is 
implied by the video output format of the image generation hardware.
The combined image generation computation latency and display system
latency measure is known as the VISUAL LATENCY. 

Questions of latency in IRIS Performer applications may refer to
either total latency or visual latency. The application developer will 
select the scope (in the sense of the four tasks outlined above) of 
the application, and then the latency will be decided by the choice of 
multiprocessing mode, frame rate, and video output format, as shown
below.


Multiprocessing and Latency
---------------------------

Multiprocessing is a major performance feature for applications based
on IRIS Performer. Multiprocessing has an effect on latency that must
be understood, however, so that increasing throughput using multiple 
processes does not cause objectionable latency. Here are the major 
multiprocessing opportunities:

  1. Application processing, such as input device measurement and
     vehicle dynamics computation for future frames can proceed in 
     parallel with image generation for current frames. These are 
     the non-visual aspects of simulation systems. These tasks were 
     once commonly performed in separate computers from different 
     vendors. The current trend is to combine this processing into 
     a single system for additional price and programming benefits.
     The latencies of these tasks are accounted for independently 
     of the visual system latency.

  2. Intersection detection, often called "mission functions" in
     the image generation world, can be performed on separate
     processors in parallel with visual simulation. 

  3. Systems with multiple graphics pipelines can operate those
     graphics systems in parallel. This can double or triple the
     total graphics throughput of a system. In essence, this means 
     operating multiple visual systems in a single box, which has 
     price and programming benefits, but does not increase latency 
     when sufficient processing power is configured.

  4. The image generation task can be subdivided into a culling
     phase and a drawing phase, and these can operate in parallel
     on separate processors to (in some cases) double throughput.
     Interestingly this is the only multiprocessing issue that has
     an impact on the latency of the visual system.

Each of the multiprocessing concepts outlined above is supported by 
IRIS Performer: application processing, intersection detection, and 
multiple graphics pipelines with parallelized cull and draw for each 
can all be realized on separate processors for increased performance.


Task Partitioning
-----------------

There are four basic ways the application, intersection, cull, and draw 
tasks can be partitioned in IRIS Performer applications. They are listed 
in the following table, with the symbol 'A' representing application 
processing, 'I' for intersections, 'C' for culling, and 'D' for drawing:

   CPU 1     CPU 2     CPU 3    pfMultiprocess Mode
  -------   -------   -------   -------------------
  A+I+C+D                       PFMP_APPCULLDRAW
   A+I+C       D                PFMP_APPCULL_DRAW
    A+I       C+D               PFMP_APP_CULLDRAW
    A+I        C         D      PFMP_APP_CULL_DRAW

As you can see, the names are built by inserting an underscore into the 
string "APPCULLDRAW" wherever this pipeline is split across multiple 
processors.

Each of the four task partitionings listed above has a twin in which the
intersection processing is performed in one or more separate processes.
These modes each require one extra process, as shown in the following
table:

  CPU 1   CPU 2   CPU 3   CPU 4    pfMultiprocess() Mode
  -----   -----   -----   -----    ---------------------
  A+C+D     I                      PFMP_APPCULLDRAW | PFMP_FORK_ISECT
   A+C      D       I              PFMP_APPCULL_DRAW | PFMP_FORK_ISECT
    A      C+D      I              PFMP_APP_CULLDRAW | PFMP_FORK_ISECT
    A       C       D       I      PFMP_APP_CULL_DRAW | PFMP_FORK_ISECT


Temporal Structure
------------------

Once the division of tasks among processors is defined, the next issue
is the temporal structure--the layout of these processes in time.
Rather than measure time in seconds, the following discussion refers to
it in terms of video frames, since these form the basic unit of time
for image generation tasks. Here is a chart showing advancing time from
left to right as measured in video frames, and within this context, the
arrangement of application, culling, and drawing in time:

       <-frame time->|
       +-------------+-------------+-------------+-------------+
 A+I   |A0->         |A1->         |A2->         |A3->         |
  C    |    C0->     |    C1->     |    C2->     |    C3->     |
  D    |        D0-> |        D1-> |        D2-> |        D3-> |
       +-------------+-------------+-------------+-------------+-->
       0             1             2             3             4

       <-- frame 0 -->
		     <-- frame 1 -->

This shows that during the time for frame 0, the first activity was
application processing (A0), followed by culling (C0), and then drawing
(D0). Note that the cull started as soon as the application finished, 
and that the draw started as soon as the cull finished. This would be
accomplished by the pfMultiprocess(PFMP_APPCULLDRAW) call, where the 
tasks are serial steps taken by one process. This mode has an elapsed 
time that is the reciprocal of the frame time. This is not the highest
throughput choice, however. A different arrangement is shown below:

       <-frame time->|
       +-------------+-------------+-------------+-------------+
 A+I   |A0---------->|A1---------->|A2---------->|A3---------->|
  C    |             |C0---------->|C1---------->|C2---------->|
  D    |             |             |D0---------->|D1---------->|
       +-------------+-------------+-------------+-------------+-->
       0             1             2             3             4

       <---------------- frame 0 --------------->
                     <---------------- frame 1 --------------->

Here, an entire frame time has been allocated for each of application, 
cull, and draw processing. This means that the complete processing for a
single frame extends across several frame times, increasing the elapsed
time from stimulus to response but also increasing the throughput of
the visual system by allowing more time for each stage of processing.

Since there are multiple processes operating in parallel (application,
culling, and drawing) the latency can be longer than 1/frame time, even 
though frames are completed at the frame rate. This is an important point 
to understand about pipelining. This mode of operation can be selected
with pfMultiprocess(PFMP_APP_CULL_DRAW).


Calculating Latency
-------------------

To calculate the visual latency of IRIS Performer applications we must
define the stimulus and response to be used.

The proper stimulus for the visual system measurement is the end of
application processing, since it is the point in time at which control
is handed to IRIS Performer for the computation of the next image. The
application processing which proceeds this point is application time;
time spent in input device measurement, in intersection processing, and
in vehicle dynamics computation. This time is important and contributes 
to total latency, but must be counted separately.

The response typically considered to terminate the latency calculation
in visual simulation is the point in time at which the last pixel of the 
first field of the new image is displayed. Understanding this requires
a brief review of video output terminology. 

A complete video image is known as a FRAME, and a frame is composed of 
one or more FIELDS. The two most common video formats used by IRIS 
Performer applications are the 60 Hertz non-interlaced display typical 
of computer workstations and the 30 Hertz frame, 60 Hertz field, 
interlaced NTSC video format used by broadcast television.

In the non-interlaced case, there is one field per frame, so the lines 
on the display are scanned sequentially from top to bottom. This means
that at a 60 Hz frame rate, each frame (and thus field) requires 1/60th
second to display. In this situation the "last pixel of the first field"
metric outlined above will be reached 1/60th second after the start of
the display of a frame.

Interlaced displays are different, in that they make multiple passes
through the image, displaying the even-numbered scan-lines on one trip
and the odd-numbered lines on the other. Each of these passes is known
as a field, and since there are two fields per frame, the field rate is
twice the frame rate. In the NTSC example, the frame rate is 30 Hz, but
the field rate is 60 Hz, so the "last pixel of the first field" event
will occur 1/60th second after the start of the display of a frame.

With these definitions of terms and events, the following timing chart
can be understood:

       <field>|
       <---frame---->|
       +------+------+------+------+------+------+------+------+
 A+I   |A0->         |A1->         |A2->         |A3->         |
  C    |    C0->     |    C1->     |    C2->     |    C3->     |
  D    |        D0-> |        D1-> |        D2-> |        D3-> |
  V    |             |V0F1->|V0F2->|V1F1->|V1F2->|V2F1->|V2F2->|
       +------+------+------+------+------+------+------+------+-->
       0      1      2      3      4      5      6      7      8

            <- F0 Latency ->
		          <- F1 Latency ->

Note that now each frame of the previous charts is now broken into two
fields and that displaying the two fields is shown as an event on the
bottom line, where 'V' represents video scan-out. Notice also that the
latencies are shown now, at the bottom of the chart. They measure the
time elapsed between the end of application processing (which is the
same as the start of the cull -- it's the point where pfFrame() is
called in the application process) up to the time when the last pixel
of the first field of the new image is displayed. This is the true 
visual latency.

The following charts illustrate the latency calculations for several
commonly used IRIS Performer multiprocessing modes. The last mode 
listed shows the advantage of overlapped cull and draw processing. In
this mode, IRIS Performer achieves the lowest visual latency reported 
for an image generation system.


Latency in PFMP_APP_CULLDRAW mode
---------------------------------

       <field>|
       <---frame---->|
       +------+------+------+------+------+------+
 A+I   |        A0-->|        A1-->|        A2-->|
  C    |             |C0---->      |C1---->      |
  D    |             |      D0---->|      D1---->|
  V    |             |             |V0F1->|V0F2->|
       +------+------+------+------+------+------+-->
       0      1      2      3      4      5      6

                <-a->|<-b-->|<-c-->|<-d-->|

 The latency for 30 Hz frame and 60 Hz display refresh rate is:
   a: application time (not our issue, can be near zero)
   b&c: culling and drawing: one frame (1/30 sec) [C0+D0 in chart]
   d: display: one field (1/60 sec) 
   --------------------------------
		    Total 3/60 sec = 50.000 msec + user app time

   Image  Field  Latency
   -----  -----  -------
   60 Hz  60 Hz  33.333 msec + user app time
   30 Hz  60 Hz  50.000 msec + user app time
   20 Hz  60 Hz  66.667 msec + user app time


Latency in PFMP_APP_CULL_DRAW mode
----------------------------------

       <field>|
       <---frame---->|
       +------+------+------+------+------+------+------+------+
 A+I   |        A0-->|        A1-->|        A2-->|        A3-->|
  C    |             |C0---------->|C1---------->|C2---------->|
  D    |             |             |D0---------->|D1---------->|
  V    |             |             |             |V0F1->|V0F2->|
       +------+------+------+------+------+------+------+------+-->
       0      1      2      3      4      5      6      7      8

                <-a->|<-----b----->|<-----c----->|<-d-->|

 The latency for 30 Hz frame and 60 Hz display refresh rate is:
   a: application time (not our issue, can be near zero)
   b: culling: one frame (1/30 sec) [C0 in above chart]
   c: drawing: one frame (1/30 sec) [D0 in above chart]
   d: display: one field (1/60 sec) 
   --------------------------------
		    Total 5/60 sec = 83.333 msec + user app time

   Image  Field  Latency
   -----  -----  -------
   60 Hz  60 Hz  50.000 msec + user app time
   30 Hz  60 Hz  83.333 msec + user app time
   20 Hz  60 Hz  116.67 msec + user app time

Latency in PFMP_APP_CULLoDRAW mode
----------------------------------

       <field>|
       <---frame---->|
       +------+------+------+------+------+------+
 A+I   |        A0-->|        A1-->|        A2-->|
  C    |             |C0--------->.|C1--------->.|
  D    |             |.D0--------->|.D1--------->|
  V    |             |             |V0F1->|V0F2->|
       +------+------+------+------+------+------+-->
       0      1      2      3      4      5      6

                <-a->|<-----b----->|
		     |<-----c----->|<-d-->|

 The latency for 30 Hz frame and 60 Hz display refresh rate is:
   a: application time (not our issue, can be near zero)
   b&c: culling and drawing: one frame (1/30 sec) [C0+D0 in chart]
   d: display: one field (1/60 sec) 
   --------------------------------
		    Total 3/60 sec = 50.000 msec + user app time

   Image  Field  Latency
   -----  -----  -------
   60 Hz  60 Hz  33.333 msec + user app time
   30 Hz  60 Hz  50.000 msec + user app time
   20 Hz  60 Hz  66.667 msec + user app time

 In this last mode the fields may be interlaced or non-interlaced. If 
 they are interlaced, then only half the frame need be computed in each 
 field. i.e. 1024x1024 rendered as 1024x512 odd lines and then as 
 1024x512 even lines. This mode of operation halves the pixels draw in
 each field, thus preserving the depth complexity of the image by
 comparison to a non-interlaced display.