TITLE:  
  perfly.doc

SUBJECT:
  Various stuff I've seen with perfly, the "Performer Town", and
  "Performer Village" demos.

AUTHOR:
  Allan Schaffer
  aschaffe@sgi.com

 - IRIX 5.0:  several customers reported that perfly would cause 
   their Onyx RE or VTX to hang.  This wasn't reproduceable here 
   and when they upgraded to IRIX 5.0.1 the problem went away.

 - IRIX 5.0.1:  perfly would generate floating point exceptions
   due to a bug in the font manager library (libfm).  This was
   fixed in 5.1.

 - "pfInit():  mmap failed for /dev/zero".  This means that you
   tried to run a Performer 1.0 application (such as a 4.x version of
   perfly) on a machine running IRIX 5.x.  Virtual memory management
   is different in IRIX 5.x, so as a workaround:

   % setenv PFTMPDIR /usr/tmp

 - Jerky forward motion, or uneven frame rate when stationary.  
   Most of the time this happens because perfly is not being run 
   as root.  When run by root, Performer applications will set 
   nondegradable priorities for their processes to improve the 
   consistency of the run-time behavior.

   Sometimes this same problem is caused by the user having another
   GL-based application (like gr_osview) running at the same time. 

 - Ghosting.  Several customers have asked why they see, as they
   turn, multiple images of objects like trees, house edges, etc.
   This is a form of "temporal aliasing" and is an attribute of
   having a frame rate which is less than the video refresh rate.

   The problem is that a single image is scanned out onto the monitor
   several times before being changed.  The repetition of a frame
   means that the image is temporally inaccurate for motion.  Real
   moving objects do not stay in one place for a couple frame times
   and then move.  

   What's actually happening is that your eye is following an object,
   moving with the same angular velocity, which keeps the image
   stationary on the retina.  Between two video refreshes of the same
   frame, your eye has moved, but the image on the screen has not.
   Consequently the image of the second frame appears at a different
   location on the retina, and you see a "ghost" image.

   So a simulation running at 20Hz update on a display refreshing at
   60Hz, the object will appear tripled.  On large objects such as
   horizon silhouette, the effect manifests itself as multiple edges.

 - what are those .tlf files ?

   The original town and village databases were built under a 
   non-distribution agreement that forced the database files to
   be shipped in an encrypted format that only the pre-compiled
   version of perfly could read.

   Unencrypted versions of the town and village databases will
   be shipped with Performer 1.2.